## Slide 1
TEAM NAME
Minesweepers Competition 2026
13th Edition
Category

## Slide 2
Minesweepers 13th Edition · Watad Ejust
2
THE CHALLENGE
The mission and our answer
The arena demands
Our design response
Rough 20 × 20 m arena: sand, grass, inclines, ditches
Tracked chassis with 15 cm wide tracks
Buried 10 cm cubes (≤ 10 cm deep) and 5 cm surface cubes
Metal detector + camera with on-laptop vision
Light and siren on every detection
Light + siren fire on every metal hit
Automatic mine map on a 19 × 19 grid (A–S, 1–19)
Kalman localization + automatic mapping
Collect the surface mines
Autonomous pickup sequence: arm + electromagnet
No Wi-Fi and no power provided at the arena
Onboard access point, 2 × 10 Ah LiPo
Notes: Source: Minesweepers 2026 rulebook, Academia category. Each design choice in this talk traces back to one of these requirements.

## Slide 3
Minesweepers 13th Edition · Watad Ejust
3
OVERVIEW
Robot at a glance
80 × 75 × 46 cm
Length × width × height
2 × 250 W
24 V geared track motors
Pi 4 + STM32
High-level + real-time control
2 × 10 Ah
LiPo battery packs
Own Wi-Fi
Onboard access point
ROS 2
Robot and base station
Notes: Teleoperated tracked UGV. Final mass is still being measured; the rule limit is 40 kg.

## Slide 4
Minesweepers 13th Edition · Watad Ejust
4
01
Mechanical Systems & Robot Structure
Body structure
Why tracks over wheels on sand
Track construction and drive train
Arm and autonomous pickup
Built for sand and heat

## Slide 5
Minesweepers 13th Edition · Watad Ejust
5
MECHANICAL
Body structure
1
Two track pods
Each pod carries its own motor, chain drive, idlers and road wheels.
2
Central spine
Bridges the pods and carries the electronics, control panel and arm.
3
Low and wide
80 × 75 × 46 cm footprint keeps the centre of gravity low between the tracks.
Notes: Left: rear view with both track loops and the spine. Right: bare chassis showing idlers and road wheels.

## Slide 6
Minesweepers 13th Edition · Watad Ejust
6
MECHANICAL
Why tracks over wheels on sand
Chart: Ground pressure (kPa) vs robot mass
| 20 kg | 30 kg | 40 kg (rule limit)
Tracks | 1.1 | 1.6 | 2.2
4 wheels | 9.8 | 14.7 | 19.6
Contact estimates: 2 tracks × 0.60 m × 0.15 m vs 4 wheels × 10 × 5 cm patch.
≈ 9× lower ground pressure
Floats on loose sand: the long footprint spreads the load instead of digging in.
Traction: every slat is a grouser biting into sand and grass.
Bridges ditches and stones that would trap a small wheel.
Trade-off: skid-steer turns need more torque, so we use 250 W geared motors.
Notes: Ground pressure p = m·g / contact area. The 0.6 m contact length per track is an estimate from the 195 cm track loop; replace it with the measured value. The comparison holds at any final mass.

## Slide 7
Minesweepers 13th Edition · Watad Ejust
7
MECHANICAL
Track construction
1
Aluminium slats
Extruded profile with a stepped edge that acts as a grouser.
2
Chain drive
The chain carries motor torque from the sprocket to every slat.
3
Rubber grip layer
Rubber sheet with cuts so it fits around the slats and grips the sand.
Track loop 195 cm · width 15 cm · white idlers on top, road wheels below carry the load
Notes: Two layers with two jobs: the chain transmits torque, the rubber sheet adds grip. Cuts in the sheet let it sit flush around each slat.

## Slide 8
Minesweepers 13th Edition · Watad Ejust
8
MECHANICAL
Drive train
Motor | MY1016Z brushed DC gear motor, 2 units
Origin | Electric wheelchair drive, sourced locally
Supply | 24 V DC
Rated power | 250 W each, 500 W total
Gearbox | Integrated reduction, high output torque
Current | ≈ 10.4 A each at rated output (250 W ÷ 24 V)
Transmission | Chain from gearbox shaft to track sprocket
Skid steering
Same speed on both tracks drives straight; a speed difference turns the robot, down to turning in place. The STM32 mixes the forward and turn commands.
Notes: Specs from the MY1016Z listing (24 V, 250 W). Repurposed wheelchair motors gave high torque on a student budget.

## Slide 9
Minesweepers 13th Edition · Watad Ejust
9
MECHANICAL · DISPOSAL
Arm design: one joint, free-hanging end
Chassis
upright
g
Single joint
driven by the wiper motor
Magnet
+ mine
Free-hanging end
gravity keeps the magnet down
1
One degree of freedom
A single rotary joint driven by the wiper motor: one motor, one limit switch, no arm kinematics to solve.
2
Free-weight end
The electromagnet hangs from a free pivot, so gravity keeps it facing the ground at any arm angle, even on a slope.
3
Simple, effective control
Only two positions, lowered and upright, with the upright switch as the reference: easy for the STM32 to control reliably.
Notes: Design choice: fewer actuators and sensors means fewer failure points in sand and heat, and a control problem small enough for the STM32 to run autonomously.

## Slide 10
Minesweepers 13th Edition · Watad Ejust
10
MECHANICAL · DISPOSAL
Autonomous pickup sequence
1
Trigger
Operator presses Pick up (J) once. The GUI sends it only if the arm reads upright.
2
Lower
The wiper motor swings the arm down over the surface mine.
3
Grab
The electromagnet is energised and the arm lifts the steel cube.
4
Stow
The magnet releases the mine into the container; the arm returns upright.
Arm motor: WD1160-series wiper motor
12 V DC · aluminium die-cast gearbox · two speeds
Rated 21.5–28 rpm, 5.2–13.2 N·m (peak up to 15 N·m) depending on variant and speed
Runs autonomously
Once triggered, the STM32 runs every step with no operator input. An upright limit switch blocks a new pickup until the arm is back.
Notes: Datasheet: M&C WD1160 / WD1160-B wiper motor, performance at rated 12 V.

## Slide 11
Minesweepers 13th Edition · Watad Ejust
11
MECHANICAL · ROUGH ENVIRONMENT
Built for sand and heat
Sand and rough terrain
Low ground pressure keeps the robot on top of loose sand
Slat grousers + rubber grip layer for traction on sand and grass
Long track footprint bridges ditches and stones
Tested outdoors on sand and grass
Heat
Electronics sit inside the chassis, shaded from direct sun
Drive motors cruise well below their 250 W rating
LiPo temperature checked between runs; spare pack ready
Notes: Confirm the heat measures with the team before presenting; the arena is outdoors in Egypt.

## Slide 12
Minesweepers 13th Edition · Watad Ejust
12
02
Electronic Components & Control System
Sensors and microcontrollers
Why an STM32 for real-time control
Power architecture and budget
On-robot and robot-to-station links
Layered safety stops

## Slide 13
Minesweepers 13th Edition · Watad Ejust
13
ELECTRONICS
Sensors and controllers
Component | Role | Interface
Raspberry Pi 4 | ROS 2, localization, video streaming | Main computer
STM32 Black Pill | Motor PWM, encoders, ADC, arm, magnet, watchdog | UART to Pi
Wheel encoders | Track odometry | STM32 timers
MPU-9250 IMU | 9-axis: accelerometer, gyro, magnetometer | I2C to Pi
Metal detector | Buried and surface mines | Analog to STM32 ADC
USB camera | Surface-mine vision and operator view | USB to Pi
Motor drivers | 2 × 250 W track motors + arm motor | PWM from STM32
Electromagnet + limit switch | Mine pickup, arm-upright interlock | STM32 I/O
Light + siren | Signal every detection | Digital output
Wi-Fi access point | Robot's own network to the base station | Network
Notes: Real-time I/O lives on the STM32; anything that needs Linux, ROS or a camera lives on the Pi.

## Slide 14
Minesweepers 13th Edition · Watad Ejust
14
ELECTRONICS
Why an STM32 for real-time control
1
Hardware encoder timers
Quadrature counting in hardware: no lost counts at full track speed.
2
Deterministic timing
A bare-metal control loop with fixed timing for PWM, sampling and the watchdog.
3
12-bit ADC
Samples the metal-detector signal for clean threshold detection.
4
Dedicated to control
Networking lives on the Pi and the onboard AP; the MCU only runs real-time I/O.
Notes: STM32 Black Pill. It talks to the Pi over UART with COBS framing and enforces the 250 ms motor watchdog.

## Slide 15
Minesweepers 13th Edition · Watad Ejust
15
ELECTRONICS
Power architecture
2 × 10 Ah
LiPo packs
Main switch
+ E-stop buttons
24 V
bus
Motor drivers
2 × MY1016Z, 250 W each
24 → 12 V converter
Wiper arm motor · electromagnet · light + siren
24 → 5 V converter
Raspberry Pi 4 → camera, IMU, STM32
Access point supply
Robot Wi-Fi network
E-stop first: every load sits downstream of the hardware stop.
High-current drive path is kept separate from the regulated logic supplies.
Notes: Check the pack wiring (series vs parallel) and converter ratings with the electronics lead before presenting.

## Slide 16
Minesweepers 13th Edition · Watad Ejust
16
ELECTRONICS · COMMUNICATION
Pi to STM32 link
Raspberry Pi 4
ROS 2 hardware-interface node
STM32 Black Pill
Real-time firmware
Down: drive (forward, turn) · pickup
Up: encoder counts · metal level · arm upright
UART frame
COBS byte
type
payload (packed struct)
checksum
0x00
COBS framing
Zero bytes appear only as the delimiter, so the receiver always resynchronises on the next frame.
Checksum
A corrupted frame is dropped, never acted on.
250 ms watchdog
No valid command for 250 ms → the STM32 sets motor PWM to zero.
Notes: Structs are packed so the 32-bit MCU and the 64-bit Pi agree on the byte layout.

## Slide 17
Minesweepers 13th Edition · Watad Ejust
17
ELECTRONICS · COMMUNICATION
Robot to control station: our own network
Robot
Onboard Wi-Fi access point
Raspberry Pi 4
ROS 2 nodes · RTSP server
STM32 + sensors
Base station (outside the fence)
Laptop joins the robot's AP
ROS 2 bridge
Docker
GUI + vision
ROS 2 DDS
drive at 20 Hz · odometry · metal · arm
RTSP video, H.264
kept out of DDS to save bandwidth
Why on the robot? The arena provides no Wi-Fi, so the link is the same in the lab and at the competition.
Notes: The 20 × 20 m arena diagonal is about 28 m plus the distance to the base station; the AP rides on the robot so range is set by our own hardware.

## Slide 18
Minesweepers 13th Edition · Watad Ejust
18
ELECTRONICS
Power budget
Chart: Rated power per load (W)
| STM32 + sensors + camera* | Light + siren* | Wi-Fi access point* | Raspberry Pi 4 | Electromagnet* | Arm wiper motor | Track motors (2 × 250 W)
Rated W | 3.5 | 5 | 6 | 7.5 | 12 | 67 | 500
Motor values from datasheets (wiper: 12 V × 5.6 A). *Estimates, to be measured.
≈ 600 W
Peak, all loads at rating
≈ 230 W
Match average (drive at ~40 %)
≈ 75 Wh
Energy for one 20 min run
≈ 3 runs
From ≈ 222 Wh on board**
**Assumes the two 10 Ah packs form one 22.2 V (6S) bus. Peak ≈ 27 A, well inside the packs' discharge rating.
Notes: Replace the starred estimates with measured currents. Battery energy depends on the pack configuration.

## Slide 19
Minesweepers 13th Edition · Watad Ejust
19
CONTROL SYSTEM
Stopping is layered
1
GUI focus lost
Drive zeroed, speed lock cleared
2
GUI refresh
No UI update for 200 ms → zero
3
ROS bridge
Drops commands > 200 ms old, publishes one zero
4
Raspberry Pi
Own motion timeout
5
STM32 watchdog
250 ms without valid frame → PWM 0
6
Hardware E-stop
Cuts power to the loads
Laptop → robot
Every stage fails safe on its own. A lost link, hung GUI or crashed process stops the robot, and reconnecting never resumes motion: the operator must press a key again.
Notes: These are per-stage timeouts, each independent of the others.

## Slide 20
Minesweepers 13th Edition · Watad Ejust
20
03
Software Stack
Architecture: STM32, Pi and laptop
Mapping and localization
Mine detection and classification
Control station GUI
Navigation plan and reliability

## Slide 21
Minesweepers 13th Edition · Watad Ejust
21
SOFTWARE
Architecture: three tiers, one contract
STM32 firmware
Raspberry Pi 4 · ROS 2 in Docker
Base-station laptop
Real-time loops
PWM · encoders · ADC · arm sequence · watchdog
Hardware interface
IMU filter (Madgwick)
Kalman filter
RTSP video server
ROS 2 bridge (Docker)
Control panel GUI
Vision: ONNX Runtime
UART
DDS
Wi-Fi
RTSP
ZeroMQ IPC
One packed, versioned C++ header shared by GUI, bridge and vision
Separate processes
An inference stall or bridge crash can't freeze the GUI
Notes: Kalman output is /odometry/filtered. The GUI owns mine mapping; the bridge only translates.

## Slide 22
Minesweepers 13th Edition · Watad Ejust
22
SOFTWARE
Mapping and localization
A
D
G
J
M
P
S
1
4
7
10
13
16
19
R
Buried
Surface
1
Localize
Kalman filter fuses track odometry (STM32 encoders) with the MPU-9250 heading. No GPS.
2
Re-anchor
At a known corner the operator resets x, y and snaps the heading to the nearest 90°.
3
Place the mine
Robot pose + detector offset (dx, dy), rotated by heading θ:
xₘ = x + dx·cos θ − dy·sin θ
yₘ = y + dx·sin θ + dy·cos θ
4
Merge and persist
Hits within a merge radius are one mine; records survive a restart. The map is generated automatically.
Notes: 19 × 19 map, columns A–S and rows 1–19, as the rulebook requires. Map frame: origin at the start corner, +X right, +Y up, heading 0 along +X.

## Slide 23
Minesweepers 13th Edition · Watad Ejust
23
SOFTWARE
Mine detection and classification
Metal detector
rising edge
Camera → ONNX
fresh vision result?
Light + siren
on every metal hit
Metal + camera sees a box
SURFACE
Mapped, then the autonomous pickup sequence collects it
Metal + camera sees nothing
BURIED
Mapped at its position; the arm is not used
Vision alone never creates a mine: the metal detector must confirm it.
Notes: The single-class object detector runs in ONNX Runtime on the laptop.

## Slide 24
Minesweepers 13th Edition · Watad Ejust
24
SOFTWARE
Control station GUI
1
Camera feed
Live RTSP video from the robot
2
Field map
Mines placed automatically as they are found
3
Drive controls
Arrow keys with smooth ramp; Space locks speed
4
Pick up mine (J)
Starts the autonomous pickup; disabled until the arm is upright
5
Link health
Stale data greyed out, never shown as zero
Notes: C++20 with Raylib for drawing and GStreamer for video. Layout and colours come from styles.toml, so they can be changed without recompiling.

## Slide 25
Minesweepers 13th Edition · Watad Ejust
25
OPERATION
Arena navigation plan
S
R
R
R
S start corner · R pose reset at a corner
1
Start in a corner
Pose reset to the known corner before the first lane.
2
Lawnmower sweep
Parallel lanes, spacing = detector width minus overlap, so no strip of the field is missed.
3
Stop, signal, classify
Light and siren fire on every metal hit; surface mines are picked up on the spot.
4
Re-anchor at every corner
Each lane end near a corner resets drift.
5
Budget the 20 minutes
Sweep time ≈ (19 m / lane spacing) × 19 m / speed, planned to cover the whole field.
Notes: Lane spacing and cruise speed come from field tests with the real detector.

## Slide 26
Minesweepers 13th Edition · Watad Ejust
26
SOFTWARE
Built to be reliable
1
One contract
A single versioned C++ header defines every message the GUI, bridge and vision process exchange.
2
Validate everything
Wrong size, version, flag, range or non-finite float: the message is dropped.
3
Dockerized robot stack
Host networking for DDS, devices found at boot, config bind-mounted so we can tune on site without rebuilding.
4
Tested
Unit and integration tests cover drive ramping, pickup gating, message decoding and the ZeroMQ link.
Notes: Telemetry arrives at 20 Hz; any source silent for 500 ms is marked stale.

## Slide 27
Minesweepers 13th Edition · Watad Ejust
27
TEAM
Team, budget and next steps
Watad Ejust
Academia category
Mechanical · electronics · software
Budget-minded build
Wheelchair drive motors and a car wiper motor bought from the local market; an open-source software stack.
After the competition
Autonomous navigation: coverage planning on top of the existing localization
Onboard vision on a Jetson; the GUI protocol stays the same
Notes: Add team member names and the total spend if the jury asks.

## Slide 28
Thank You